## Slide 1: Cost-Effective High Voltage Motor Controller for Automotive Use
sdmay25-26 Bryce Rega, Marek Jablonski, Gavin Patel, Jonah Frosch, Long Yu
May 7th, 2025
Cheng Huang (chengh@iastate.edu)
Notes: Marek

## Slide 3: Problem Statement
There exists a market gap in lightweight EV motor controllers
  Used in collegiate solar cars and electric bikes
These unique applications have unique specs
  Low RPM (0-1000)
  High Torque (Direct Drive)
  High/Medium Voltage (48-135V)
  Medium Power (Peak ~7.5KW)
Problem: Existing controllers
  Are very expensive (~$7k each)
  Black boxes to those who use them
  Notorious for having issues.
Electric bike in-hub motor
ebikeling.com
PRISUM's solar car, P15 Eliana
PRISUM Media Archive
Notes: Marek

## Slide 4: Functional Requirements
Operational
  Spin Motor in either direction
  Current and/or speed controlled
Electrical
  0-900rpm Electrical Rotation speed
  48-135VDC Power Input
  50A Bus Draw
  200A Peak Coil Current
    High Torque Output
Communication
  CAN bus command/status IO
    Used in large interconnected vehicles
  GPIO interface
    Simple Bare-bones operation
CAN Node Diagram
CAN bus - Wikipedia
Mitsuba 2096-III Motor
Marek Jablonski
Notes: Marek

## Slide 5: Nonfunctional Requirements
Compact and Lightweight
  200x200x100mm outer dimension
  Less than 4kg
Environmental Resistance
  0°-45°C Operating ambient
  Water-resistant connectors
Aesthetics
  Useful Labeling
  Professional Design
User Experience
  Comprehensive Documentation and Guides
  External Configuration Utility
Existing hookup Diagram
Mitsuba M2096 Controller Manual
Mitsuba 2096C Controller
Marek Jablonski
Notes: Marek

## Slide 6: Other Considerations
Open-Source Design
  Removes Overhead from User Cost
  Enables Cost cuts for resourceful Users
Safety
  Dangerous Voltages/Energy
  Electrical Isolation
  Energy Dissipation
  Cautions/Warnings
Example Hazard Label
Safety in Motor Maintenance and Troubleshooting – Monolithic Power System
https://www.flickr.com/photos/lintmachine/2333562855
Notes: Marek

## Slide 7: Project Overview
Custom High Voltage Motor Controller
Low Total cost for controller when compared to market options
Develop some user interface for interfacing and configuring controller
Compatible with many different applications
M2096 kit
Mitsuba M2096 Controller Manual (OEM Recommended Controller)
Mitsuba 2096-III Motor
(Application Motor)
Wavesculpter 22 Controller
(Aftermarket Controller)
Notes: Gavin

## Slide 8: Concept Sketch
Notes: Gavin

## Slide 9: Development Phases
Development Board
Revision 1
Revision 2
Get familiar with software via examples
Setup hardware configurations
Partially meet requirements
Test hardware to learn for next revision
Test basic custom software
Completely meet requirements
Final deliverable
Notes: Bryce Rega

## Slide 10: Development Board Results (Fall 2024)
Determined test motor parameters
  Coil Inductance
  Internal Resistance
  Winding and Pole/Pair Scheme
Too Low Torque
  Could barely spin up motor
  Frequent OC faults
Control Scheme Issues
  Not configured for this motor type
Development Board Failed
  Gate Driver internal failure
  Necessary information gained beforehand
Notes: Long Yu
During testing, we found improved motor parameters, particularly in terms of coil inductance and internal resistance and the winding and pole/pair scheme. However, the Development Board encountered torque limitations. The motor could barely spin up, and we frequently experienced overcurrent faults. Another challenge was with the control scheme, which was not configured optimally for this specific motor type. Lastly, the Development Board failed due to an internal gate driver failure. But, we had already gathered the necessary information about motor parameters and system behavior before this happened, this will be helpful in guiding our next steps.

## Slide 11: Revision 1 Software Design
Software Design Diagram
MCU Pinout
Notes: Bryce Rega

## Slide 12: Revision 1
Logic Board Top Level
Logic Board MCU
High Voltage Capacitor Bank
Power Board Top Level
Power Board
  Main Board, Contains all high power circuitry
Logic Board
  Daughter Board to Power Board, Contains MCU
Notes: Marek

## Slide 13: Revision 1 Design
Current Layout of Rev 1 Logic Board
Switching Characteristics simulation
3D View of Rev 1 Layout
Schematic for the MCU in Rev 1
Notes: Marek

## Slide 14: Revision 1 Outcome
Hardware issues identified for revision 2
  Capacitors didn't meet specification
    ~50% less than expected
  Lack of test points, labels on board
  Pinout for MCU incorrect
  Floating Outputs Present under Reset
Software In Progress
  Spun slowly (~30rpm) at a fixed speed
  Fasters speeds non-functional
  No current/torque based control
  Analog throttle input functional
Rev 1 Temporary fixes implemented
Jonah Frosch
February 2025
Notes: Bryce Rega

## Slide 15: Revision 2 Pinout
Phase PWM channels are swapped
  Built in features on MCU
Additional I/O
  Buttons, LEDs, Serial
Move throttle analog channel
More debug pins
Pin Name/Func Peripheral Pin Name/Func Peripheral
Notes: Bryce Rega

## Slide 16: Revision 2 Design
Power Board Layout Top
Logic Board Layout Top
Power Board layout Bottom
Logic Board Layout Bottom
Power Board Rev. 2
Logic Board Rev. 2
Notes: Jonah

## Slide 17: Logic Schematic
Top Level Schematic
Microcontroller Schematic
Power Converter Schematic
Notes: Jonah

## Slide 18: Power Board Rev. 2 Schematic
High Voltage Capacitor Bank
Gate Drivers
Gate Driver + Gates
Notes: Jonah

## Slide 19: Gate Driver Design
Gate Driver
Notes: Jonah

## Slide 20: Testing
Hardware Testing
  Connectivity and Capacitor Performance Verification
  High voltage tests to verify gate driver operation
Software Testing
  Verify PWM operation is as expected
  Test rotation speeds and their efficiency
  Control over CAN communication
Notes: Gavin

## Slide 21: Revision 2 Outcome
Hardware Progress
  Operationally Performed as Expected
  Larger than expected voltage fluctuations at input
    Likely due to using SMPS at input instead of Battery
    Fixed with large Electrolytic capacitor bank
Software Progress
  PWM Control from stall to ~1050rpm
  Analog throttle control
  No current/torque based control
Notes: Long Yu
In Revision 2, we addressed several key hardware and software challenges. On the hardware side, we encounter larger than expected voltage fluctuations at input. It is likely due to the use of switch mode power supply instead of a battery. This was resolved using a large electrolytic capacitor bank, allowing the system to operate as expected. On the software side, we successfully implemented PWM control, achieving speeds up to 1050 rpm, and also board level analog and CAN input. However, current and torque-based control is still pending.

## Slide 22: Demonstration
Notes: Long Yu

## Slide 23: Project Costs
Senior Design Cost Breakdown ($) | 
PCBs | $198.30
PCB Components | $517.06
Dev Board | $104.86
Ext. Capacitor | $50
Misc. Hardware | $17.95
Heatsink Estimate | $65
Total | $949.67
Product Cost Per Unit Breakdown($) | 
PCBs | $20.88
PCB Components | $318.92
Misc. Hardware | $17.92
Heatsink Estimate | $65
Total | $422.75
Notes: Jonah44

## Slide 24: Challenges and Lessons Learned
Reputable sources give more accurate specifications
Building software for multi-platform support takes time
  Likely not worth using the limited time in senior design for it
Communication of expectations
  Hardware didn't know what software didn't know
  Software thought they knew what hardware wanted but didn't
Notes: Bryce Rega

## Slide 25: Future Work
High Load Testing
  Build/Setup Test Dyno
  On-vehicle Testing
  Unable to perform High-Load Testing
    Late Timeline
    Unavailability of a test Dyno
    Test Vehicle Expects Current/Torque based control
Deeper Hardware Testing
  Power Supply Variations
    Battery/Power Supply, Ceramic, Electrolytic combinations
  Analyse Switching Power Loss
    Different Gate Drive parameters
    Loss/gain from additional gates
PID Current Control
  Target a current instead of Duty Cycle
  Tuning
  Controlled regenerative braking
Improved Control Theory
  Sinusoidal drive function
    "Shuffle" away from 6-step trapezoidal
  Field Oriented Control
Notes: Gavin

## Slide 26: Contributions
Marek
Simulations and applications expertise
Jonah
Component selection, Schematic design and Layout design
Bryce
Fixed dev-board example code, developed control layers and tests
Gavin
Developed board level drivers, began development for GUI
Long
Reasearch and order parts, updated documents and websites
Notes: Jonah

## Slide 27: Questions?

## Slide 28: Further Technical Details
Additional content to support what was covered in the high-level slides

## Slide 29: Simulation schematic

## Slide 30: Simulation waveform

## Slide 31: SAM C21 J18 Pinout

## Slide 39: Motor Reference Images

## Slide 40: Controller Reference Images

## Slide 41: Engineering Standards
  IEEE 1547 - Standard for Interconnecting Distributed Resources with Electric Power Systems
    This standard outlines requirements for safely interconnecting distributed energy resources (like solar and wind) with electric power systems, focusing on performance, safety, and reliability.
  IEEE 1149.1 - Standard Test Access Port and Boundary-Scan Architecture
    This standard defines a boundary-scan architecture for testing and debugging integrated circuits and circuit boards, allowing access to internal signals for easier diagnostics without physical probes.
  IEEE 1554 - Standard for Software Engineering in the Life Cycle of Digital Systems
    This standard provides guidelines for software engineering throughout the life cycle of digital systems, emphasizing structured practices for development, Detroit testing, and maintenance to improve software quality and reliability.